## Slide 1
MEG and EEG analysis using
October 2023

## Slide 2: Brainstorm
Free and open-source application
Matlab & Java: Platform-independent
Designed for Matlab
Stand-alone version available
Interface-based: click, drag, drop
No programming experience required
Daily updates of the software
Supports most common file formats

## Slide 3: Graphic interface

## Slide 4: Workflow
EEG/MEG
Anatomy
Co-registration
Sensors
Source estimation
Analysis
Averages
Contrasts
Group analysis
Time-frequency
Connectivity

## Slide 5: Single subject
Importing
Pre-processing
Analysis of the
experimental data
Loop: all acquisition runs all subjects
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Events
Epoching
Averaging
Sources
Time-frequency

## Slide 6: Import
One-click import of the T1 segmentation: FreeSurfer, BrainSuite, BrainVISA, CIVET, CAT
Import and place fiducials in the MRI (N,L,R)
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency

## Slide 7: Database
Three levels:
  Protocol
  Subject
  Condition
Popup menus
All files saved in Matlab .mat
Same architecture on the disk

## Slide 8: Import
Original files linked to the database (no copy)
Rich data viewer with flexible montage editor
Optimized reading functions
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency

## Slide 9: Co-registration MEEG / MRI (1)
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Basic estimation based on three points: Nasion (NAS), Left ear (LPA), Right ear (RPA)
MRI: Marked in the volume with the MRI Viewer
MEEG: Obtained with a tracking system (Polhemus)

## Slide 10: Co-registration MEEG / MRI (2)
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Automatic adjustment based on head shape: Fitting Polhemus points on the MRI head surface
Final registration must be checked manually
Polhemus driver included in Brainstorm

## Slide 11: Quality control
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Power spectrum density for quality control
< 3Hz: Eyes
10Hz: Alpha
50/60Hz
> 40Hz: Muscle
MEG
Bad channels
EEG

## Slide 12: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Notch filter: Removes 50Hz/60Hz power line noise (and harmonics)
PSD
Signal

## Slide 13: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
High-pass filter: Removes slow components (eye movements, breathing, sensor drifts…)
Low-pass filter: Remove high-frequencies

## Slide 14: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Manual inspection of the recordings
Interactive selection of bad channels
Re-reference the EEG if necessary (Average ref)

## Slide 15: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Automatic detection of blinks and heartbeats (peak detection, or explicit amplitude threshold)
ECG
EOG
ECG
EOG

## Slide 16: Artifact correction
Two categories of artifacts:
  Well defined, reproducible, short, frequent:
    Heartbeats, eye blinks, eye movements, some stimulators
    Unavoidable and frequent: we cannot just ignore them
    Can be modeled and removed from the signal efficiently
  All the other events that can alter the recordings:
    Movements, building vibrations, metro nearby…
    Too complex or not repeated enough to be modeled
    Safer to mark them as bad segments, and ignore them

## Slide 17: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Correction with Signal Space Projections (SSP)
PCA
Spatial components
Detect artifacts
Select components and compute a linear projector to remove their contribution from the recordings

## Slide 18: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Example: Cardiac artifact
Original
SSP

## Slide 19: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Example: Blink

## Slide 20: Pre-processing
Independent component analysis (ICA):
  Popular in the EEG literature
  Alternative to SSP for low number of sensors
  Already implemented: Infomax and JADE (EEGLAB)

## Slide 21: Pre-processing
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Automatic detection of artifacts (RMS-based)
Manual screening of all the recordings is advised (scroll all the sensors by pages of 10-20s)
Exclude: Blinks, movements, SQUID jumps

## Slide 22: Elekta-Neuromag SQUID jumps
Sharps steps followed by a change of baseline value
Mark the channels as bad before running MaxFilter
Or mark the segments as bad in Brainstorm

## Slide 23: Epoching
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Presentation
Sensor
Manual
Two types of experiments:
  Steady-state or resting-state (ongoing activity)
  Event-based (stimulus, response, spike…)
How to get event markers in the recordings?

## Slide 24: Epoching
Reading the triggers saved by the presentation software (includes jittered OS delays)
File triggers are never aligned with the real stim
Stimulation software
Operating system
Video or
sound card
Projector
Image production (jittered delays)
Triggers
MEG signals
.fif
Transmission (fixed or jittered)
Recording (fixed delays)
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Presentation
Sensor
Manual

## Slide 25: Epoching
Reading information recorded on the subject side (photodiode, microphone, response box…)
Avoids most uncontrollable jittered delays
Stimulation software
Operating system
Video or
sound card
Projector
Image production (jittered delays)
MEG signals
.fif
Transmission (fixed or jittered)
Photodiode signal
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Presentation
Sensor
Manual
Recording (fixed delays)
Triggers

## Slide 26: Epoching
Reading the triggers save by the presentation software (includes jittered OS delays)
Reading information recorded on the subject side (photodiode, microphone, response box)
Manual or automatic marking of biological or behavioral events, post-acquisition (epileptic spikes, sleep spindles, rat position in a box…)
Optimized workflow for clinicians (keyboard and mouse shortcuts, workspace…)
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Presentation
Sensor
Manual

## Slide 27: Epoching
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Combine
Extract
Length
Process
In some experiments, the event of interest is a combination of presentation markers.
Example: Priming experiments
In Brainstorm, the events of interest are saved as new marker types in the continuous files.
In other environments, the events are sometimes defined only at the epoching time and not saved in the continuous file.
A C B C B C A C Markers
E1 E2 E2 E1 Events

## Slide 28: Epoching
In Brainstorm, the events of interest are saved as new marker types in the continuous files.
In other environments, the events are sometimes defined only at the epoching time and not saved in the continuous file.
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Combine
Extract
Length
Process

## Slide 29: Epoching
Epochs = Trials = Short blocks of recordings around an event of interest.
Epoching = Extracting epochs from the continuous recordings and saving them.
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Combine
Extract
Length
Process

## Slide 30: Epoching
In Brainstorm, each imported epoch is an independent file in the database.
Accessible by event type or individually.
In other programs, all the epochs from one run are saved in one single file (one file per event type, or one file with all the events).
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Combine
Extract
Length
Process

## Slide 31: Epoching
How to define the optimal epoch length ?
Experimental design: Expected effect duration, inter-stimulus interval
Analysis: Frequency filters and amplitude normalizations may require longer epochs
Computational limitations: Size and time
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Combine
Extract
Length
Process
[0,900] ms
+ 200ms baseline
+ 300ms filters
= [-500, 1200] ms

## Slide 32: Epoching
Processing steps that can be applied on epochs:
  DC offset correction: Subtract the average estimated over a baseline period
  Detrending: Subtract a linear trend estimated over a reference period
  Resampling: Decrease the sampling rate
This dataset: DC correction, baseline=[-500,0]ms
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Combine
Extract
Length
Process

## Slide 33: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Averaging the trials: Reveals the features of the signals that are locked in time to a given event = Event-related field / potential = Evoked response = ERF/ERP
MEG
EEG

## Slide 34: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
EEG: Averaging data across runs and subjects OK.
MEG: Averaging across runs is not always accurate
  Head shapes differ between subjects.
  Head positions different between runs.
  One sensor does not record the same thing in two different runs.
  Coregistration of runs with Elekta MaxFilter helps but modifies a lot the recordings. Never use this to average across subjects.
  Recommended: Estimate the sources for each run separately, then average in source space.

## Slide 35: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
EEG ERP: Famous faces

## Slide 36: Single subject
Sensor space: EEG or MEG sensors
Source space: Cortex or full head volume
Forward model: Overlapping spheres (MEG) OpenMEEG BEM/DUNEuro FEM (EEG)
Inverse model: Minimum norm estimates Beamformers Separately for MEG and EEG
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Inverse
Forward
Source space
Sensor space

## Slide 37: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
The MNE model requires an estimation of the level of noise of the sensors
Noise covariance matrix = covariance of segments that do not contain any “meaningful” data
Empty room, pre-stim baseline, resting
T

## Slide 38: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Famous faces
MEG
EEG
MEG sources

## Slide 39: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Regions of interest at cortical level (scouts) = Subset of a few dipoles in the brain = Group of vertices of the cortex surface

## Slide 40: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Dipole scanning Compute a distributed source model, then find the most significant dipole at each time sample.
Dipole fitting (FieldTrip) Non-linear search of the dipoles that minimizes the residuals (data explained - recordings)

## Slide 41: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Faces – Scrambled, 160ms

## Slide 42: Source estimation: MEG
Recommended in MEG analysis:
  The subject head can move in the helmet
  One sensor is not corresponding to one brain region
  Different types of sensors (magneto / gradiometers)
  Difficult to read, reproduce or compare
Converting to source space helps solving those issues
M.Hamalainen 2007

## Slide 43: MEG sensors
CTF (MNI)
275 axial gradiometers
Elekta (MIT)
204 planar gradiometers
102 magnetometers

## Slide 44: Source estimation: EEG
In EEG, those problems don’t exist:
  Electrodes positions are fixed and known
  More reproducible signal shapes and topographies
  Clinicians are trained to work at the sensor level
But the source reconstruction is still interesting:
  Localize the signal generators in the brain
  (epilepsy and pre-surgical functional mapping)
  Spatial separation of simultaneous sources

## Slide 45: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Morlet wavelets
Hilbert transform + band-pass filter

## Slide 46: Single subject Sub002 / R01
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Make sure you know the transient periods for all the frequency bins, and do not include them in your analysis.
An easy solution is to cut them out immediately after the computation.

## Slide 47: Time-frequency Average

## Slide 48: Time-frequency

## Slide 49: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Other measures
Phase-amplitude coupling

## Slide 50: Single subject
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Other measures
Connectivity measures
Correlation
Coherence
Phase locking value
Granger causality

## Slide 51: Group analysis
Normalize
(TF and sources)
Anatomy
Link recordings
MRI registration
PSD
Filters
Bad channels
Artifacts
Correction
Bad segments
Markers
Epoching
Averaging
Sources
Time-frequency
Weighted avg
Run averages
Subject averages
Group averages
Statistical tests
Low-pass filter
Project to template (sources only)
N subjects x M runs
N averages

## Slide 52: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Weighted average of 6 runs per subject (recordings, sources MEG/EEG, time-frequency)
Sources: Compute within-subject differences
  (Faces - Scrambled) and (Famous - Unfamiliar)
  The sign of the MNE source amplitude is ambiguous, we will apply an absolute value before comparing between subjects

## Slide 53: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Low-pass filter the subject averages: 32Hz
Remove 300ms on each side (edge effects)

## Slide 54: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
  Amplitude normalization before group analysis Baseline = [-200,0]ms
Sources: Z-score normalization wrt baseline S = (S – mean(baseline)) / std(baseline)
Time-frequency: Event-related sync/desync TF = (TF – mean(baseline)) / mean(baseline) * 100

## Slide 55: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Using FreeSurfer registration
Subject
Template
3D interpolation
FreeSurfer registration
FreeSurfer registration

## Slide 56: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Using BrainSuite registration
Subject
Template
3D interpolation
BrainSuite registration
BrainSuite registration

## Slide 57: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Registration of individual sources on a template (ICBM152, Colin27, DNI, infants…)
Subject 1
Subject 2
Individual anatomy
Standard anatomy
Group analysis
Average Contrast
…

## Slide 58: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Faces - Scrambled
MEG
EEG
EEG 070
MEG Z>3
EEG Z>3
ROI EEG
ROI MEG

## Slide 59: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Faces - Scrambled
Permutation t-test, 1000 rand, p<0.05 FDR-corrected
MEG
EEG
FieldTrip cluster test, cluster alpha=0.05, 1000 rand
EEG
Parametric Chi2-test log(|Faces-Scrambled|)=0 p<0.05 FDR-corrected
MEG
EEG

## Slide 60: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Contrasts between subjects or conditions
Parametric t-test
Cluster-based non-parametric tests
Export to: SPM, R, Excel, SPSS, Matlab…

## Slide 61: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
When scripting the analysis, we recommend you always check visually the following items for each run separately:
  MRI/sensors registration
  PSD before and after filters
  SSP and ICA component topographies
  ERP/ERF: Sensors time series
  ERP/ERF: Sensors topo of primary response
  ERP/ERF: Sources of primary response
  Any other metric of interest

## Slide 62: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Execution reports with snapshots saved in HTML

## Slide 63: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Prototype the analysis interactively with one subject. Write down all the parameters to reproduce with a script.
Set the anatomical fiducials for all the subjects.
Script #1: Import the anatomy for all the subjects
Script #2: Pre-processing (loop on subjects)
  Link the raw files, register with MRI, compute PSD
  Detect or import event markers
  Pre-processing: Filtering, detect artifacts, SSP, ICA
Manual inspection:
  Check the execution reports for script 2
  Fix the SSP/ICA (re-compute, manual selection)
  Mark bad channels and bad segments

## Slide 64: Group analysis
Subject averages
Low-pass
Normalize
Project
Group averages
Group statistics
Quality control
Workflow
Script #3: Subject-level analysis (loop on subjects)
  Importing and averaging
  Source estimation
  Time-frequency
Manual inspection:
  Check the execution reports for script #3
  Define regions of interest
Script #4: Group analysis
  Subject-level averages
  Group-level averages
  Statistics
  Anything that involves regions of interest

## Slide 65: Add your code to Brainstorm
Direct manipulation of the files in Matlab
Use the menu “Run Matlab command”
Write a plugin:
  Well documented API
  Lots of example (170 functions written as plugins)
  Open-source GitHub repository
Examples of recent external contributions:
  MVPA decoding (Oliva, MIT)
  Microstate segmentation (Cacioppo, UChicago)
  Eyetracker/EEG synchronization (Uni Freiburg)

## Slide 66: User community (2023)
40,000+ users registered on the website

## Slide 67: User support
Online tutorials: 30-hour self-training program
Active user forum: 150 posts/month
Daily updates: 1500 downloads/month
@BrainstormSoftware
@brainstorm2day
@brainstorm-tools

## Slide 68: Contributors
Richard Leahy
USC
Sylvain Baillet
MNI
John Mosher
Cleveland Clinic
Investigators
Elizabeth Bock
MEGIN, Chicago
Dimitrios Pantazis
MIT
Collaborators
Anand Joshi
RA Professor
Hossein Shahabi
Research assistant
McGill
Jeremy Moreau
PhD student
Soheila Samiee
PhD student
François Tadel
Software, Grenoble
Engineers
Raymundo Cassani
Software, MNI
Marc Lalancette
MEG manager, MNI
Konstantinos Nasiotis
Post-doc
USC
Takfarinas Medani Research assistant
Guiomar Niso
Politécnica Madrid
Juan García-Prieto Martinos Ctr, MGH
Christophe Grova Concordia
Thomas Vincent
Montreal Heart Inst.
Edouard Delaire
Concordia
NIRSTORM

## Slide 69: Next Brainstorm Workshop
April 1st – 4th 2024
Park city, ut, usa
www.AIEPILEPSY-NEURO.com
2nd International Conference on
Artificial Intelligence in Epilepsy
and Neurological Disorders
Algorithms, machine learning, deep learning and artificial intelligence in epilepsy and neurological disorder clinical care, practice and research with special emphasis on devices, wearables, apps and platforms
This year on April 1st we will also hold a special Workshop on the Brainstorm Platform for Clinicians and Scientists and its use in Stereotactic EEG and Epilepsy Surgery
Organizing Committee:
Sam Lhatoo MD, Philippe Ryvlin, Michael Sperling, Sandor Beniczky
For any information: Aiepilepsy-neuro@ant-congres.com

## Slide 70: Team today
Raymundo Cassani
Takfarinas Medani
Woojae Jeong
Chinmay Chinara
John
Mosher
Richard Leahy

## Slide 71: Workshop dataset
  Visual recognition task
Faces presentation: Famous / Unfamiliar / Scrambled
1 participant / 1 run / aprox. 50 trials per condition
400-600ms fixation cross, 800-1000 stim, 1700ms ISI Total 10min per run
Elekta-Neuromag VectorView system (MEG+EEG) 102 magnetometers, 204 gradiometers, 70 electrodes Recorded at 1100Hz
• Individual MRI, anonymized, processed with FreeSurfer 5.3

## Slide 72: Workshop dataset
  Median nerve stimulation
Right arm stimulation: monophasic square-wave duration 0.3 ms at 2.8 Hz
1 participant / 1 run / 336 stimuli
Individual MRI, processed with CAT12
MEG: Yokogawa 160 axial gradiometers @ 2000 Hz
EEG: Nihon Kohden 41 electrodes @ 2000 Hz
Median nerve percutaneous stimulation
Simultaneous MEG and EEG acquisition
EEG electrodes and MEG helmet
Scalp and cortical surface

## Slide 73: Acquisition setup
Stimulation
computer
Acquisition
computer
MEG and EMG
Stim